## Slide 1: OPC UA
OPC UA Server generated from model with MQTT client
Wolfgang Hottgenroth 2016-06-09

## Slide 2: Title here again in Arial 24 max. one line
Agenda
Topic here, Arial 20
Topic here, max. one line
Topic here, use boldness for marking
Topic here, move the triangle for marking
Topic here, do not use more than 10 topics
Topic here, keep it simple

## Slide 3: OPC UA Creation of Model
  Model created with UaModeler (Unified Automation GmbH)
  First, a “type” has to be created

## Slide 4: OPC UA Creation of Model
  Second, based on that type an instance has to be created

## Slide 5: OPC UA Creation of Model
  Model exported into XML format (OPC UA XML Schema)
<UANodeSet xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:uax="http://opcfoundation.org/UA/2008/02/Types.xsd" xmlns="http://opcfoundation.org/UA/2011/03/UANodeSet.xsd" xmlns:s1="http://krohnegroup.com/TestModel/Types.xsd" xmlns:xsd="http://www.w3.org/2001/XMLSchema"> <NamespaceUris> <Uri>http://krohnegroup.com/TestModel/</Uri> </NamespaceUris> […] <UAObjectType NodeId="ns=1;i=1002" BrowseName="1:TemperatureSensorType"> <DisplayName>TemperatureSensorType</DisplayName> <References> <Reference ReferenceType="HasComponent">ns=1;i=5001</Reference> <Reference ReferenceType="HasComponent">ns=1;i=5006</Reference> <Reference ReferenceType="HasComponent">ns=1;i=5002</Reference> <Reference ReferenceType="HasSubtype" IsForward="false">i=58</Reference> </References> </UAObjectType> <UAObject ParentNodeId="ns=1;i=1002" NodeId="ns=1;i=5001" BrowseName="1:Configuration"> <DisplayName>Configuration</DisplayName> <References> <Reference ReferenceType="HasTypeDefinition">i=58</Reference> <Reference ReferenceType="HasComponent" IsForward="false">ns=1;i=1002</Reference> <Reference ReferenceType="HasComponent">ns=1;i=6001</Reference> <Reference ReferenceType="HasModellingRule">i=78</Reference> </References> </UAObject> […]
Can be easily created using KDDB Generator
Required structure information is available in KDDB

## Slide 6: OPC UA Generation of Code
  open62541 (Open Source Stack for Server and Client) provides tool to generate C-code from XML
TestModel.c: testmodel.xml ./tools/pyUANamespace/generate_open62541CCode.py \ tools/schema/namespace0/Opc.Ua.NodeSet2.xml $^ TestModel TestModel.h: TestModel.c myTestModelServer.o: myTestModelServer.c TestModel.h myTestModelServer: myTestModelServer.o TestModel.o $(CC) -o $@ $(CFLAGS) $(LDFLAGS) $^ $(LIBS) -lmosquitto .c.o: $(CC) $(CFLAGS) -c $<
  Namespace 0 of OPC UA needs to be created into C-code too, since it contains basic definitions required in specific model
  Created C-file is large:

## Slide 7: OPC UA Server Code - Initialization
  Server code is rather simple
int main(int argc, char** argv) { signal(SIGINT, stopHandler); /* catches ctrl-c */ /* initialize the server */ UA_ServerConfig config = UA_ServerConfig_standard; UA_ServerNetworkLayer nl = UA_ServerNetworkLayerTCP(UA_ConnectionConfig_standard, 16664); config.networkLayers = &nl; config.networkLayersSize = 1; UA_Server *server = UA_Server_new(config);

## Slide 8: OPC UA Server Code – Loading and “bonding” the model
Main() continued:
TestModel(server); UA_DataSource uptimeDataSource = (UA_DataSource) { .handle = &upTime, .read = readInteger, .write = 0}; UA_Server_setVariableNode_dataSource(server, UA_NODEID_NUMERIC(2, 6006), uptimeDataSource); UA_DataSource measuredTemperatureDataSource = (UA_DataSource) { .handle = &measuredTemperature, .read = readDouble, .write = 0}; UA_Server_setVariableNode_dataSource(server, UA_NODEID_NUMERIC(2, 6004), measuredTemperatureDataSource);
uint32_t upTime = 0;
static UA_StatusCode readInteger(void *handle, const UA_NodeId nodeid, UA_Boolean sourceTimeStamp, const UA_NumericRange *range, UA_DataValue *dataValue) { dataValue->hasValue = true; UA_Variant_setScalarCopy(&dataValue->value, handle, &UA_TYPES[UA_TYPES_INT32]); return UA_STATUSCODE_GOOD; }

## Slide 9: OPC UA Server Code – Running the server
Main() continued:
UA_StatusCode retval = UA_Server_run_startup(server); if (retval == UA_STATUSCODE_GOOD) { while (running == true) { upTime = time(0); measuredTemperature += 0.25; // dummy value uint16_t canWait = 0; canWait = UA_Server_run_iterate(server, 0); struct timeval timeout = { .tv_sec = 0, .tv_usec = canWait * 1000 }; select(0, 0, 0, 0, &timeout); } }

## Slide 10: Thank you for your attention!